NTC Design Technology Risk Assessment

| Task to be assessed: Woodwork and Metal work vices |
| --- |
| Location – DT Workshops | Risk assessor – Richard Shrimpton | Assessment date – Friday 1st sept 23 |
| Next review date: Friday 1st sept 24 | Approved by CL: | Assessor Signed: |

| Hazard / Risk | Who is at risk? | Normal Control Measures (Brief description and/or reference to source of information). | Additional Control Measures (to take account of local/individual circumstances). | Risk Rating H/M/L |
| --- | --- | --- | --- | --- |
| Manual handling | All users Dropping on feet or injuring back | Vices usually are heavy and if moving to put into position proper manual handling techniques should be used | Students to ask an adult who knows manual handling to move the vice | H |
| Crush or nipping/ pinching injuries | All users | Single user operation at all times Usage of common sense when using the vice ie: do not insert fingers between jaws or the workpiece Bench stop is enclosed on three sides to minimise finger injury from fingers getting caught. | Soft jaws can be used in some circumstances (metal vice) | H |
| Storage | All Users | When not in use and if appropriate, make sure the vices are stored in a store room or appropriate safe area to minimise the risk of tripping over it and it falling from its position. | Teacher in charge to make sure this is done | M/H |
| Clothes snagging | All in class | Close jaws of vices loosely when not in use Ensure bench vice is restored to the fixed, down position when finished with | Teacher in charge to make sure this is done | L/M |
| Sharp edges on vice jaws | All users | Technicians to ensure all vice jaws are maintained and are deemed safe to use, although it is the users responsibility to report damaged goods | Ensure all sharp edges are adressed and fixed or ja2ws are removed from use | L |
| Screws or general debris wedged or impaled into wooden vices | All users | Teachers and technicians responsible for up keep of vices. Teachers in class and technicians to repair | Teachers and technicians to regularly check vices for debris | L/M |