Risk Assessment : Brazing hearth and chip forge

| Location: DT Workshops (Room 0-206) | Date assessment undertaken: 24/02/2015 | Assessment undertaken by: Richard Shrimpton |
| --- | --- | --- |
| Activity or situation: Brazing hearth and chip forge | Review date: 20/02/15 | Signature: |

| (1) Hazard | Risk | (2) Who might be harmed and how | (3) What Controls exist to reduce the risk | (4) What action can be taken to further control the risk |
| --- | --- | --- | --- | --- |
| Electric Shock | L | All in room | Electrical safety testing PAT Yearly | Has electrical isolation |
| Risk of injury (burns) | H | All operatives Blowtorch And ceramic chip forge | Wear goggles Tie long hair back Wear apron Wear task appropriate footwear Wear heat and flame resistant gloves | Only staff trained to use machines, use safely and pass knowledge on to students. Course on workshop safety |
| Clothing | M | All operatives | Ensure that loose items of clothing are tucked away. | Wearing of overalls |
| Inhalation of fumes | M/H | All in room | Control of materials and chemicals used (MSDS available). Ensure brazing hearth extration is working properly and is switched on when machine is in use. | Open doors and increase air flow in local area |
| Jogging, Tripping or distraction to machine operative | H | All operatives | Caution Tape on floor 1m away from machine for adequate room allowance | Safety talks and good housekeeping practice |
| Ceramic chips sticking to material being heated and dropping on to the floor | M | All operatives | Regular inspection and replacement of unsuitable ceramic chips | Concrete floor so floor covering will not ignite |
| Risk of fire in room | H | All in room | Good working practice | Staff and students to report any defects to technicians for them to take appropriate action. Any incandesent materials to be moved far enough away as to decrease the risk of ignition to a minimum |