Thomas Tallis Design Technology Risk Assessment

| Task to be assessed: Useage of Hand Drills (Manual) |
| --- |
| Location – DT Workshops | Risk assessor – Richard Shrimpton | Assessment date – Friday 13th Feb 2015 |
| Next review date:13th Feb 2016 | Approved by CL: | Assessor Signed: |

| Hazard / Risk | Who is at risk? | Normal Control Measures (Brief description and/or reference to source of information). | Additional Control Measures (to take account of local/individual circumstances). | Risk Rating H/M/L |
| --- | --- | --- | --- | --- |
| Walking around the classroom with a drill bit in the drill | All in class Stabbing / getting cut | When transporting the hand drill always detacth drill bits, and place them back in the rack | Students to be vigilant of other students not obeying the rule described adjacent Good housekeeping | H |
| Nipping / Pinching of the hand when using the drill and/or inserting the drill bit. Tightening the chuck | Students, Technicians and teachers | Students told the correct way, by the teacher in charge, of loading / unloading a drill bit to minimise the risk of injury (Hold drill handle and operation handle using one hand and tighten the chuck with the other hand) | It is essential that when loading a dill bit that it is central in the chuck to ensure correct clamping of the drill bit | M |
| Storage | Teachers and Technicians | Tool specific storage is available in each room, the drills should be unloaded and stored here when not in use. | Tool cupboards are fittesd with a lock and should be locked when not in use | L |
| Drill bits breaking while being used | Teachers and Technicians | Good instruction and guidance from teacher in order to keep the drill directly horizontal / vertical when in use | Drill stand has been made available from the technicians Side handle is available if needed | H |
| Damaged drills | All users | Drills to be maintained by the technicians | Students and teachers to report faulty drills to technicians | M |