NTC Design Technology Risk Assessment – Generic super glue and activator

| Task to be assessed: Generic Super glue and Activator |
| --- |
| Location – DT, ALL Areas | Risk assessor – Richard Shrimpton | Assessment date – 1/9/23 |
| Next review date:1/9/24 | Approved by CL: | Assessor Signed: |

| Hazard / Risk | Who is at risk? | Normal Control Measures (Brief description and/or reference to source of information). | Additional Control Measures (to take account of local/individual circumstances). | Risk Rating H/M/L |
| --- | --- | --- | --- | --- |
| Inhalation of fumes from both glue and Activator Composition: ethyl 2-cyanoacrylate 1,4-dihydroxybenzene | All people in room | Keep room well ventilated Ask students if any of them in the class suffer from any known allergic reactions to the products, and/ or Asthma. Teacher to action | Lids and caps to be replaced after usage immediately. When using the Activator Spray, spray downwards to the floor, minimising airborne particles Remedial: Move person to fresh air and remove the source of Inhalation from the immediate vicinity. Encourage deep breaths to flush out aerosol. If respiratory problems persist, seek medical advice, and show container. | M |
| Skin contact (Activator) | User | When using the Activator Spray, spray downwards to the floor, minimising airborne particles Wash hands with soap and water | Over exposure to the skin can cause dryness. Wash hands with soap if this is the case. Continued application to the skin, can cause freeze burn. . If any problems persist, seek medical advice, and show container. | L |
| Skin contact (super glue) | User and surroundings | Skin bonding to skin or other object Make sure any spillages are cleaned up with a Cloth, not paper towel, as it will soak through quickly to the hand. Contact the DT technician immediately (First Aid) Skin will heat up due to chemical reaction, then will subside. If the skin is bonded to other skin or surface, do not try to remove. And seek first aid for help. | Lids replaced after use, Only use a small amount at a time. Both activator and Glue to be signed out from technician, to make sure they do not get left in classes and abused / stolen Debonder kept with technician and only to be used to debond skin to skin or skin to object. if a small amount of super glue is on skin only and not bonded to anything, wash hands with soap and leave to wear off over time. (Sweating will speed up this process.) this loosens the glue from the skin | H |
| General First Aid measures: | ALL affected. | General advice : Move out of dangerous area. Consult a physician. Show this safety data sheet to the doctor in attendance. If inhaled : Move to fresh air. Consult a physician after significant exposure. In case of skin contact : Take off contaminated clothing and shoes immediately. Wash off with soap and plenty of water. If symptoms persist, call a physician. In case of eye contact : Immediately flush eye(s) with plenty of water. Remove contact lenses. Keep eye wide open while rinsing. If eye irritation persists, consult a specialist. If swallowed : Do not induce vomiting without medical advice. Rinse mouth with water. Do not give milk or alcoholic beverages. Never give anything by mouth to an unconscious person. | Make sure First aider is present to access the situation. | N/A |
|  |  | For more info, see MSDS sheet on NTC website www.dtntc.weebly.com |  |  |